## Slide 1: Chapter 2: outline
2.1 principles of network applications
  app architectures
  app requirements
2.2 Web and HTTP
2.3 FTP
2.4 electronic mail
  SMTP, POP3, IMAP
2.5 DNS
2.6 P2P applications
2.7 socket programming with UDP and TCP

## Slide 2: DNS: domain name system
people: many identifiers:
  SSN, name, passport #
Internet hosts:
  “hostname”, e.g., www.yahoo.com - used by humans
  IP address (32 bit) - used for addressing datagrams (Chapter 4), e.g., 121.7.106.83
Q: how to map between IP address and name, and vice versa ?
Domain Name System:
distributed database implemented in hierarchy of many name servers
application-layer protocol: hosts, name servers communicate to resolve names (address/name translation)
  note: core Internet function, implemented as application-layer protocol
  complexity at network’s “edge”

## Slide 3: DNS: services, structure
why not centralize DNS?
single point of failure
traffic volume
distant centralized database
maintenance
DNS services
hostname to IP address translation
host aliasing
  canonical, alias names
mail server aliasing
load distribution
  replicated Web servers: many IP addresses correspond to one name

## Slide 4: DNS: a distributed, hierarchical database
Root DNS Servers
com DNS servers
org DNS servers
edu DNS servers
poly.edu
DNS servers
umass.edu
DNS servers
yahoo.com
DNS servers
amazon.com
DNS servers
pbs.org
DNS servers
…
…
Top Level Domain (TLD) DNS servers

## Slide 5: DNS: a distributed, hierarchical database
Root DNS Servers
com DNS servers
org DNS servers
edu DNS servers
poly.edu
DNS servers
umass.edu
DNS servers
yahoo.com
DNS servers
amazon.com
DNS servers
pbs.org
DNS servers
…
…
authoritative DNS servers

## Slide 6: DNS: a distributed, hierarchical database
Root DNS Servers
com DNS servers
org DNS servers
edu DNS servers
poly.edu
DNS servers
umass.edu
DNS servers
yahoo.com
DNS servers
amazon.com
DNS servers
pbs.org
DNS servers
client wants IP for www.amazon.com; 1st approx:
client queries root server to find com DNS server
client queries .com DNS server to get amazon.com DNS server
client queries amazon.com DNS server to get IP address for www.amazon.com
…
…

## Slide 7: DNS: root name servers
contacted by local name server that can not resolve name
root name server:
  contacts authoritative name server if name mapping not known
  gets mapping
  returns mapping to local name server
13 root name “servers” worldwide
a. Verisign, Los Angeles CA
(5 other sites)
b. USC-ISI Marina del Rey, CA
l. ICANN Los Angeles, CA
(41 other sites)
e. NASA Mt View, CA
f. Internet Software C.
Palo Alto, CA (and 48 other sites)
i. Netnod, Stockholm (37 other sites)
k. RIPE London (17 other sites)
m. WIDE Tokyo
(5 other sites)
c. Cogent, Herndon, VA (5 other sites)
d. U Maryland College Park, MD
h. ARL Aberdeen, MD
j. Verisign, Dulles VA (69 other sites )
g. US DoD Columbus, OH (5 other sites)

## Slide 8: TLD, authoritative servers
top-level domain (TLD) servers:
  responsible for com, org, net, edu, aero, jobs, museums, and all top-level country domains, e.g.: uk, fr, ca, jp
  Network Solutions maintains servers for .com TLD
  Educause for .edu TLD
authoritative DNS servers:
  Organization’s own DNS server(s), providing authoritative hostname to IP mappings for organization’s named hosts
  can be maintained by organization or service provider

## Slide 9: Local DNS name server
does not strictly belong to hierarchy
each ISP (residential ISP, company, university) has one
  also called “default name server”
when host makes DNS query, query is sent to its local DNS server
  has local cache of recent name-to-address translation pairs (but may be out of date!)
  acts as proxy, forwards query into hierarchy

## Slide 10: DNS name resolution example
requesting host
cs.shsu.edu
gaia.cs.umass.edu
root DNS server
local DNS server
dns.shsu.edu
1
2
3
4
5
6
authoritative DNS server
dns.umass.edu
7
8
TLD DNS server
host at shsu.edu wants IP address for gaia.cs.umass.edu
In order to obtain the mapping for one hostname, 8 DNS messages were sent.

## Slide 11: DNS name resolution example
requesting host
cs.shsu.edu
gaia.cs.umass.edu
root DNS server
local DNS server
dns.shsu.edu
1
2
3
4
5
6
authoritative DNS server
dns.umass.edu
7
8
TLD DNS server
host at shsu.edu wants IP address for gaia.cs.umass.edu
In order to obtain the mapping for one hostname, 10 DNS messages were sent.
Let’s assume that each department has its own departmental DNS server. E.g. CS’ local department DNS is cs.umss.edu

## Slide 12: DNS name resolution example
requesting host
cs.shsu.edu
mail.yahoo.com
root DNS server
local DNS server
dns.shsu.edu
1
2
3
4
5
6
authoritative DNS server
dns.yahoo.com
7
8
TLD DNS server
host at shsu.edu wants IP address for mail.yahoo.com
iterated query:
User's computer: "What is the IP Address of mail.yahoo.com?"
Local name server: "I don't know that. But I'll check with a name server that does."

## Slide 13: DNS name resolution example
host at shsu.edu wants IP address for mail.yahoo.com
iterated query:
Local name server: "What is the IP Address of mail.yahoo.com?"
Root name server: "Here are the addresses for the authoritative name servers for .com."
requesting host
cs.shsu.edu
mail.yahoo.com
root DNS server
local DNS server
dns.shsu.edu
1
2
3
4
5
6
authoritative DNS server
dns.yahoo.com
7
8
TLD DNS server

## Slide 14: DNS name resolution example
host at shsu.edu wants IP address for mail.yahoo.com
iterated query:
Local name server: "What is the IP Address of mail.yahoo.com?"
TLD name server: "Here are the addresses of the authoritative name servers for yahoo.com."
requesting host
cs.shsu.edu
mail.yahoo.com
root DNS server
local DNS server
dns.shsu.edu
1
2
3
4
5
6
authoritative DNS server
dns.yahoo.com
7
8
TLD DNS server

## Slide 15: DNS name resolution example
host at shsu.edu wants IP address for mail.yahoo.com
iterated query:
Local name server: "What is the IP Address of mail.yahoo.com?"
Authoritative name server: "Here is the IP address for mail.yahoo.com, its 205.139.94.60."
requesting host
cs.shsu.edu
mail.yahoo.com
root DNS server
local DNS server
dns.shsu.edu
1
2
3
4
5
6
authoritative DNS server
dns.yahoo.com
7
8
TLD DNS server

## Slide 16
my computer
I am a root DNS server.
IP: 111.111.111.111
I am a .edu DNS server (TLD DNS server).
IP: 222.222.222.222
I am the authoritative DNS server of “www.shsu.edu”.
IP: 333.333.333.333
SuddenLink Local DNS server.
Example (1)

## Slide 17
my computer
I am a root DNS server.
IP: 111.111.111.111
I am a .edu DNS server (TLD DNS server).
IP: 222.222.222.222
I am the authoritative DNS server of “www.shsu.edu”.
IP: 333.333.333.333
SuddenLink Local DNS server.
What is the IP address of net.cs.shsu.edu?
Example (1)

## Slide 18
my computer
I am a root DNS server.
IP: 111.111.111.111
I know the IP address of the device (.edu DNS server) which knows IP addresses of devices (servers) whose host address ends with “ ~ ~.edu”.
I am a .edu DNS server (TLD DNS server).
IP: 222.222.222.222
I am the authoritative DNS server of “www.shsu.edu”.
IP: 333.333.333.333
What is the IP address of net.cs.shsu.edu?
SuddenLink Local DNS server.
Ask to 222.222.222.222
Example (1)

## Slide 19
my computer
I am a root DNS server.
IP: 111.111.111.111
I know the IP address of the device (.edu DNS server) which knows IP addresses of devices (servers) whose host address ends with “ ~ ~.edu”.
I am a .edu DNS server (TLD DNS server).
IP: 222.222.222.222
I know the IP address of the device (shsu.edu DNS server) which knows IP addresses of devices (servers) whose host address is with “shsu.edu”.
I am the authoritative DNS server of “www.shsu.edu”.
IP: 333.333.333.333
What is the IP address of net.cs.shsu.edu?
SuddenLink Local DNS server.
Ask to 333.333.333.333
Example (1)

## Slide 20
my computer
I am a root DNS server.
IP: 111.111.111.111
I know the IP address of the device (.edu DNS server) which knows IP addresses of devices (servers) whose host address ends with “ ~ ~.edu”.
I am a .edu DNS server (TLD DNS server).
IP: 222.222.222.222
I know the IP address of the device (shsu.edu DNS server) which knows IP addresses of devices (servers) whose host address is with “shsu.edu”.
I am the authoritative DNS server of “www.shsu.edu”.
IP: 333.333.333.333
I am the only DNS server for “shsu.edu” and I know the IP address for “net.cs.shsu.edu” and it is “444.444.444.444”
What is the IP address of net.cs.shsu.edu?
SuddenLink Local DNS server.
It is 444.444.444.444
Example (1)

## Slide 21
my computer
I am a root DNS server.
IP: 111.111.111.111
I know the IP address of the device (.edu DNS server) which knows IP addresses of devices (servers) whose host address ends with “ ~ ~.edu”.
I am a .edu DNS server (TLD DNS server).
IP: 222.222.222.222
I know the IP address of the device (shsu.edu DNS server) which knows IP addresses of devices (servers) whose host address is with “shsu.edu”.
I am the authoritative DNS server of “www.shsu.edu”.
IP: 333.333.333.333
I know the IP address of the device (cs.shsu.edu DNS server) which know IP addresses of devices (servers) whose host address is “ cs.shsu.edu”.
What is the IP address of net.cs.shsu.edu?
Ask to 444.444.444.444
I am the CS Dept’s (cs.shsu.edu’s) DNS server.
IP: 444.444.444.444
Example (2)

## Slide 22
my computer
I am a root DNS server.
IP: 111.111.111.111
I know the IP address of the device (.edu DNS server) which knows IP addresses of devices (servers) whose host address ends with “ ~ ~.edu”.
I am a .edu DNS server (TLD DNS server).
IP: 222.222.222.222
I know the IP address of the device (shsu.edu DNS server) which knows IP addresses of devices (servers) whose host address is with “shsu.edu”.
I am the authoritative DNS server of “www.shsu.edu”.
IP: 333.333.333.333
I know the IP address of the device (cs.shsu.edu DNS server) which know IP addresses of devices (servers) whose host address is “ cs.shsu.edu”.
I am the CS Dept’s (cs.shsu.edu’s) DNS server.
IP: 444.444.444.444
What is the IP address of net.cs.shsu.edu?
It is 555.555.555.555.
I am the only DNS server for “cs.shsu.edu” and I know the IP address for “net.cs.shsu.edu”.
Example (2)

## Slide 23
4
5
6
3
recursive query:
puts burden of name resolution on contacted name server
heavy load at upper levels of hierarchy?
requesting host
cs.shsu.edu
mail.yahoo.com
root DNS server
local DNS server
dns.shsu.edu
1
2
7
authoritative DNS server
dns.yahoo.com
8
DNS name resolution example
TLD DNS
server
Q: Which strategy, iterated query or recursive query is often used practically?

## Slide 24: DNS: caching, updating records
once (any) name server learns mapping, it caches mapping
  cache entries timeout (disappear) after some time (TTL)
  TLD servers typically cached in local name servers
    thus root name servers not often visited
cached entries may be out-of-date (best effort name-to-address translation!)
  As mapping of hostname to IP address may change, therefore the DNS server discards its cache after a certain amount of time. (2 days)

## Slide 25: DNS records
DNS: distributed db storing resource records (RR)
type=NS
  name is domain (e.g., foo.com)
  value is hostname of authoritative name server for this domain
RR format: (name, value, type, ttl)
type=A
  name is hostname
  value is IP address
type=CNAME
  name is alias name for some “canonical” (the real) name
  www.ibm.com is really
  servereast.backup2.ibm.com
  value is canonical name
type=MX
  value is name of mailserver associated with name
Time To Live
(time to remove)

## Slide 26: DNS protocol, messages
query and reply messages, both with same message format
msg header
identification: 16 bit # for query, reply to query uses same #
flags:
  query or reply
  recursion desired
  recursion available
  reply is authoritative
identification
flags
# questions
questions (variable # of questions)
# additional RRs
# authority RRs
# answer RRs
answers (variable # of RRs)
authority (variable # of RRs)
additional info (variable # of RRs)
2 bytes
2 bytes

## Slide 27
name, type fields
for a query
RRs in response
to query
records for
authoritative servers
additional “helpful”
info that may be used
identification
flags
# questions
questions (variable # of questions)
# additional RRs
# authority RRs
# answer RRs
answers (variable # of RRs)
authority (variable # of RRs)
additional info (variable # of RRs)
DNS protocol, messages
2 bytes
2 bytes

## Slide 28: Inserting records into DNS
example: new startup “Network Utopia”
register name networkuptopia.com at DNS registrar (e.g., Network Solutions)
  provide names, IP addresses of authoritative name server (primary and secondary)
  registrar inserts two RRs into .com TLD server: (networkutopia.com, dns1.networkutopia.com, NS)
  (dns1.networkutopia.com, 212.212.212.1, A)
create authoritative server type A record for www.networkuptopia.com; type MX record for networkutopia.com
Notes: Internet Corporation for Assigned Names and Numbers (ICANN) accredits the various registrars.
http://www.internic.net

## Slide 29: Chapter 2: outline
2.1 principles of network applications
  app architectures
  app requirements
2.2 Web and HTTP
2.3 FTP
2.4 electronic mail
  SMTP, POP3, IMAP
2.5 DNS
2.6 P2P applications
2.7 socket programming with UDP and TCP

## Slide 30: Socket programming
Socket API
introduced in BSD4.1 UNIX, 1981
explicitly created, used, released by apps
client/server paradigm
two types of transport service via socket API:
  unreliable datagram
  reliable, byte stream-oriented
a host-local,
application-created,
OS-controlled interface (a “door”) into which
application process can both send and
receive messages to/from another application process
socket
Goal: learn how to build client/server application that communicate using sockets

## Slide 31: Socket-programming using TCP
Socket: a door between application process and end-end-transport protocol (UCP or TCP)
TCP service: reliable transfer of bytes from one process to another
process
TCP with
buffers,
variables
socket
controlled by
application
developer
controlled by
operating
system
host or
server
process
TCP with
buffers,
variables
socket
controlled by
application
developer
controlled by
operating
system
host or
server
internet

## Slide 32: Socket programming with TCP
Client must contact server
server process must first be running
server must have created socket (door) that welcomes client’s contact
Client contacts server by:
creating client-local TCP socket
specifying IP address, port number of server process
When client creates socket: client TCP establishes connection to server TCP
When contacted by client, server TCP creates new socket for server process to communicate with client
  allows server to talk with multiple clients
  source port numbers used to distinguish clients (more in Chap 3)
TCP provides reliable, in-order
transfer of bytes (“pipe”)
between client and server
application viewpoint

## Slide 33: Stream jargon
A stream is a sequence of characters that flow into or out of a process.
An input stream is attached to some input source for the process, eg, keyboard or socket.
An output stream is attached to an output source, eg, monitor or socket.

## Slide 34: Socket programming with TCP
Example client-server app:
1) client reads line from standard input (inFromUser stream) , sends to server via socket (outToServer stream)
2) server reads line from socket
3) server converts line to uppercase, sends back to client
4) client reads, prints modified line from socket (inFromServer stream)
Client
process
client TCP socket

## Slide 35: Client/server socket interaction: TCP
wait for incoming
connection request
connectionSocket =
welcomeSocket.accept()
create socket,
port=x, for
incoming request:
welcomeSocket =
ServerSocket()
create socket,
connect to hostid, port=x
clientSocket =
Socket()
close
connectionSocket
read reply from
clientSocket
close
clientSocket
Server (running on hostid)
Client
send request using
clientSocket
read request from
connectionSocket
write reply to
connectionSocket
TCP
connection setup

## Slide 36: Example: Java client (TCP)
import java.io.*;
import java.net.*;
class TCPClient {
public static void main(String argv[]) throws Exception
{
String sentence;
String modifiedSentence;
BufferedReader inFromUser =
new BufferedReader(new InputStreamReader(System.in));
Socket clientSocket = new Socket("hostname", 6789);
DataOutputStream outToServer =
new DataOutputStream(clientSocket.getOutputStream());
Create
input stream
Create
client socket,
connect to server
Create
output stream
attached to socket

## Slide 37: Example: Java client (TCP), cont.
BufferedReader inFromServer =
new BufferedReader(new
InputStreamReader(clientSocket.getInputStream()));
sentence = inFromUser.readLine();
outToServer.writeBytes(sentence + '\n');
modifiedSentence = inFromServer.readLine();
System.out.println("FROM SERVER: " + modifiedSentence);
clientSocket.close();
}
}
Create
input stream
attached to socket
Send line
to server
Read line
from server

## Slide 38: Example: Java server (TCP)
import java.io.*;
import java.net.*;
class TCPServer {
public static void main(String argv[]) throws Exception
{
String clientSentence;
String capitalizedSentence;
ServerSocket welcomeSocket = new ServerSocket(6789);
while(true) {
Socket connectionSocket = welcomeSocket.accept();
BufferedReader inFromClient =
new BufferedReader(new
InputStreamReader(connectionSocket.getInputStream()));
Create
welcoming socket
at port 6789
Wait, on welcoming
socket for contact
by client
Create input
stream, attached
to socket

## Slide 39: Example: Java server (TCP), cont
DataOutputStream outToClient =
new DataOutputStream(connectionSocket.getOutputStream());
clientSentence = inFromClient.readLine();
capitalizedSentence = clientSentence.toUpperCase() + '\n';
outToClient.writeBytes(capitalizedSentence);
}
}
}
Read in line
from socket
Create output
stream, attached
to socket
Write out line
to socket
End of while loop,
loop back and wait for
another client connection

## Slide 40: Socket programming with UDP
UDP: no “connection” between client and server
no handshaking
sender explicitly attaches IP address and port of destination to each packet
server must extract IP address, port of sender from received packet
UDP: transmitted data may be received out of order, or lost
application viewpoint
UDP provides unreliable transfer
of groups of bytes (“datagrams”)
between client and server

## Slide 41: Client/server socket interaction: UDP
close
clientSocket
Server (running on hostid)
read reply from
clientSocket
create socket,
clientSocket =
DatagramSocket()
Client
Create, address (hostid, port=x,
send datagram request
using clientSocket
create socket,
port=x, for
incoming request:
serverSocket =
DatagramSocket()
read request from
serverSocket
write reply to
serverSocket
specifying client
host address,
port number

## Slide 42: TCP vs. UDP
TCP
Socket()
  Connection steam established: Data goes in one end of pipe and out the other. Pipe stays open until it is closed.
ServerSocket()
  A special type of socket that sits waiting for a knock from a client to open connection. Leads to handshaking.
UDP
DatagramSocket()
  Data sent as individual packets of bytes. Each packet contains all addressing info. No concept of open “pipe”.
No handshaking!
  A DatagramSocket waits to receive each packet

## Slide 43: Example: Java client (UDP)
Output: sends packet (TCP sent “byte stream”)
Input: receives packet (TCP received “byte stream”)
Client
process
client UDP socket

## Slide 44: Example: Java client (UDP)
import java.io.*;
import java.net.*;
class UDPClient {
public static void main(String args[]) throws Exception
{
BufferedReader inFromUser =
new BufferedReader(new InputStreamReader(System.in));
DatagramSocket clientSocket = new DatagramSocket();
InetAddress IPAddress = InetAddress.getByName("hostname");
byte[] sendData = new byte[1024];
byte[] receiveData = new byte[1024];
String sentence = inFromUser.readLine();
sendData = sentence.getBytes();
Create
input stream
Create
client socket
Translate
hostname to IP
address using DNS

## Slide 45: Example: Java client (UDP), cont.
DatagramPacket sendPacket =
new DatagramPacket(sendData, sendData.length, IPAddress, 9876);
clientSocket.send(sendPacket);
DatagramPacket receivePacket =
new DatagramPacket(receiveData, receiveData.length);
clientSocket.receive(receivePacket);
String modifiedSentence =
new String(receivePacket.getData());
System.out.println("FROM SERVER:" + modifiedSentence);
clientSocket.close();
}
}
Create datagram with data-to-send,
length, IP addr, port
Send datagram
to server
Read datagram
from server

## Slide 46: Example: Java server (UDP)
import java.io.*;
import java.net.*;
class UDPServer {
public static void main(String args[]) throws Exception
{
DatagramSocket serverSocket = new DatagramSocket(9876);
byte[] receiveData = new byte[1024];
byte[] sendData = new byte[1024];
while(true)
{
DatagramPacket receivePacket =
new DatagramPacket(receiveData, receiveData.length);
serverSocket.receive(receivePacket);
Create
datagram socket
at port 9876
Create space for
received datagram
Receive
datagram

## Slide 47: Example: Java server (UDP), cont
String sentence = new String(receivePacket.getData());
InetAddress IPAddress = receivePacket.getAddress();
int port = receivePacket.getPort();
String capitalizedSentence = sentence.toUpperCase();
sendData = capitalizedSentence.getBytes();
DatagramPacket sendPacket =
new DatagramPacket(sendData, sendData.length, IPAddress,
port);
serverSocket.send(sendPacket);
}
}
}
Get IP addr
port #, of
sender
Write out
datagram
to socket
End of while loop,
loop back and wait for
another datagram
Create datagram
to send to client