## Slide 1
Chapter 3 Transport Layer
Computer Networking: A Top Down Approach 6th edition Jim Kurose, Keith Ross Addison-Wesley March 2012
A note on the use of these ppt slides:
We’re making these slides freely available to all (faculty, students, readers). They’re in PowerPoint form so you see the animations; and can add, modify, and delete slides (including this one) and slide content to suit your needs. They obviously represent a lot of work on our part. In return for use, we only ask the following:
If you use these slides (e.g., in a class) that you mention their source (after all, we’d like people to use our book!)
If you post any slides on a www site, that you note that they are adapted from (or perhaps identical to) our slides, and note our copyright of this material.
Thanks and enjoy! JFK/KWR
All material copyright 1996-2012
J.F Kurose and K.W. Ross, All Rights Reserved

## Slide 2: Goals of COSC 2327
Gain factual knowledge on transport layer.
Get to know the principles of multiplexing/demultiplexing, reliable data transfer, congestion control, and flow control.

## Slide 3: Chapter 3: Transport Layer
our goals:
understand principles behind transport layer services:
  multiplexing, demultiplexing
  reliable data transfer
  flow control
  congestion control
learn about Internet transport layer protocols:
  UDP: connectionless transport
  TCP: connection-oriented reliable transport
  TCP congestion control

## Slide 4: Chapter 3 outline
3.1 transport-layer services
3.2 multiplexing and demultiplexing
3.3 connectionless transport: UDP
3.4 principles of reliable data transfer
3.5 connection-oriented transport: TCP
  segment structure
  reliable data transfer
  flow control
  connection management
3.6 principles of congestion control
3.7 TCP congestion control

## Slide 5: Transport services and protocols
provide logical communication between app processes running on different hosts
transport protocols run in end systems
  send side: breaks app messages into segments, passes to network layer
  rcv side: reassembles segments into messages, passes to app layer
more than one transport protocol available to apps
  Internet: TCP and UDP
application
transport
network
data link
physical
logical end-end transport
application
transport
network
data link
physical

## Slide 6: Transport vs. network layer
network layer: logical communication between hosts
transport layer: logical communication between processes
  relies on, enhances, network layer services
12 kids in Ann’s house sending letters to 12 kids in Bill’s house:
hosts = houses
processes = kids
app messages = letters in envelopes
transport protocol = Ann and Bill who demux to in-house siblings
network-layer protocol = postal service
household analogy:

## Slide 7: Internet transport-layer protocols
reliable, in-order delivery (TCP)
  congestion control
  flow control
  connection setup
unreliable, unordered delivery: UDP
  no-frills extension of “best-effort” IP
services not available:
  delay guarantees
  bandwidth guarantees
application
transport
network
data link
physical
application
transport
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
logical end-end transport

## Slide 8: Chapter 3 outline
3.1 transport-layer services
3.2 multiplexing and demultiplexing
3.3 connectionless transport: UDP
3.4 principles of reliable data transfer
3.5 connection-oriented transport: TCP
  segment structure
  reliable data transfer
  flow control
  connection management
3.6 principles of congestion control
3.7 TCP congestion control

## Slide 9: Multiplexing/demultiplexing
process
socket
use header info to deliver
received segments to correct
socket
demultiplexing at receiver:
handle data from multiple
sockets, add transport header (later used for demultiplexing)
multiplexing at sender:
transport
application
physical
link
network
P2
P1
transport
application
physical
link
network
P4
transport
application
physical
link
network
P3

## Slide 10: How demultiplexing works
host receives IP datagrams
  each datagram has source IP address, destination IP address
  each datagram carries one transport-layer segment
  each segment has source, destination port numbers
host uses IP addresses & port numbers to direct segment to appropriate socket
source port #
dest port #
32 bits
application
data
(payload)
other header fields
TCP/UDP segment format

## Slide 11: Connectionless demultiplexing
recall: created socket has host-local port #:
DatagramSocket mySocket1 = new DatagramSocket(12534);
when host receives UDP segment:
  checks destination port # in segment
  directs UDP segment to socket with that port #
recall: when creating datagram to send into UDP socket, must specify
  destination IP address
  destination port #
IP datagrams with same dest. port #, but different source IP addresses and/or source port numbers will be directed to same socket at dest

## Slide 12: Connectionless demux: example
Port#6428
transport
application
physical
link
network
P3
transport
application
physical
link
network
P1
transport
application
physical
link
network
P4
Port#5775
Port#9157
source port: 9157
dest port: 6428
source port: 6428
dest port: 9157
source port: ?
dest port: ?
source port: ?
dest port: ?
UDP socket identified by 2-tuple:
  dest IP address
  dest port number
Q. What is the purpose of the source port number in the UDP segment?

## Slide 13: Connection-oriented demux
TCP socket identified by 4-tuple:
  source IP address
  source port number
  dest IP address
  dest port number
demux: receiver uses all four values to direct segment to appropriate socket
server host may support many simultaneous TCP sockets:
  each socket identified by its own 4-tuple
web servers have different sockets for each connecting client
  non-persistent HTTP will have different socket for each request

## Slide 14: Connection-oriented demux: example
transport
application
physical
link
network
P3
transport
application
physical
link
P4
transport
application
physical
link
network
P2
source IP,port: A,9157
dest IP, port: B,80
source IP,port: B,80
dest IP,port: A,9157
host: IP address A
host: IP address C
network
P6
P5
P3
source IP,port: C,5775
dest IP,port: B,80
source IP,port: C,9157
dest IP,port: B,80
three segments, all destined to IP address: B,
dest port: 80 are demultiplexed to different sockets
server: IP address B

## Slide 15: Connection-oriented demux: example
transport
application
physical
link
network
P3
transport
application
physical
link
transport
application
physical
link
network
P2
source IP,port: A,9157
dest IP, port: B,80
source IP,port: B,80
dest IP,port: A,9157
host: IP address A
host: IP address C
server: IP address B
network
P3
source IP,port: C,5775
dest IP,port: B,80
source IP,port: C,9157
dest IP,port: B,80
P4
threaded server

## Slide 16: (Sec 3.1-3.2) Review Questions
Q1. A UDP socket is fully identified by:
  A. destination IP
  B. destination port number
  C. source IP
  D. source port number

## Slide 17: (Sec 3.1-3.2) Review Questions
Q2. A TCP socket is fully identified by:
  A. destination IP
  B. destination port number
  C. source IP
  D. source port number

## Slide 18: (Sec 3.1-3.2) Review Questions
Q3. True or False?
  “UDP segment with different source IP addresses and/or source port numbers but with same destination IP and port number are directed to same socket.”
  “TCP segment with different source IP addresses and/or source port numbers but with same destination IP and port number are directed to same socket.”
Notes: True
False (TCP is identified by :

## Slide 19: (Sec 3.1-3.2) Review Questions
Q4.
  Host C has UDP Socket with Port # 6789.
  Host A & Host B each send a UDP segment to Host C with destination Port # 6789.
  Will both of these segments be direct to the same socket to Host C?
Notes: Yes

## Slide 20: Chapter 3 outline
3.1 transport-layer services
3.2 multiplexing and demultiplexing
3.3 connectionless transport: UDP
3.4 principles of reliable data transfer
3.5 connection-oriented transport: TCP
  segment structure
  reliable data transfer
  flow control
  connection management
3.6 principles of congestion control
3.7 TCP congestion control

## Slide 21: Preview
UDP
  Connectionless
  Unreliable
  No Flow control
  No Congestion control
  No re-transmission
  Example: “What is past is past.”
    Game, Video, …
TCP
  Connection-oriented
  Reliable
  Flow control
    Sliding Window
  Congestion control
  Re-transmission
  Example:
    Email, FTP, …

## Slide 22: UDP: User Datagram Protocol [RFC 768]
“no frills,” “bare bones” Internet transport protocol
“best effort” service, UDP segments may be:
  lost
  delivered out-of-order to app
connectionless:
  no handshaking between UDP sender, receiver
  each UDP segment handled independently of others
UDP use:
  streaming multimedia apps (loss tolerant, rate sensitive)
  DNS
  SNMP
reliable transfer over UDP:
  add reliability at application layer
  application-specific error recovery!
Notes: Simple Network Management Protocol (SNMP)

## Slide 23: UDP: segment header
source port #
dest port #
32 bits
application
data
(payload)
UDP segment format
length
checksum
length, in bytes of UDP segment, including header
no connection establishment (which can add delay)
simple: no connection state at sender, receiver
small header size
no congestion control: UDP can blast away as fast as desired
why is there a UDP?

## Slide 24: UDP checksum
sender:
treat segment contents, including header fields, as sequence of 16-bit integers
checksum: addition (one’s complement sum) of segment contents
sender puts checksum value into UDP checksum field
receiver:
compute checksum of received segment
check if computed checksum equals checksum field value:
  NO - error detected
  YES - no error detected. But maybe errors nonetheless? More later ….
Goal: detect “errors” (e.g., flipped bits) in transmitted segment
Notes: Receiver adds all bits in the segment except for the checksum
And then adds checksum. The answer should be all 1s if not all 1s then there’s an error

## Slide 25: Internet checksum: example
example: add two 16-bit integers
1 1 1 1 0 0 1 1 0 0 1 1 0 0 1 1 0
1 1 1 0 1 0 1 0 1 0 1 0 1 0 1 0 1
1 1 0 1 1 1 0 1 1 1 0 1 1 1 0 1 1
1 1 0 1 1 1 0 1 1 1 0 1 1 1 1 0 0
1 0 1 0 0 0 1 0 0 0 1 0 0 0 0 1 1
wraparound
sum
checksum
Note: when adding numbers, a carryout from the most significant bit needs to be added to the result
Notes: Kurose and Ross forgot to say anything about wrapping the carry and adding it to low order bit

## Slide 26: (Sec 3.3) Review Questions
UDP has which of the following characteristics:
  connection state at the server
  three-way hand shake for connection establishment
  Re-transmission of packets
  none of the above

## Slide 27: (Sec 3.3) Review Questions
UDP uses 1s complement for its checksum. Suppose a sender’s segment has the following three 8-bit bytes: 01010011, 01100110, 01110100. What is ‘checksum’ in the sender’s UDP segment? (For this problem you are being asked to consider 8-bit sums, not 16-bit.)
  11010001
How does the receiver’s UDP check an error of the segment?
  The receiver adds the four words (the three original words and the checksum). If the sum contains a zero, the receiver knows there has been an error.
Notes: 

## Slide 28: Chapter 3 outline
3.1 transport-layer services
3.2 multiplexing and demultiplexing
3.3 connectionless transport: UDP
3.4 principles of reliable data transfer
3.5 connection-oriented transport: TCP
  segment structure
  reliable data transfer
  flow control
  connection management
3.6 principles of congestion control
3.7 TCP congestion control

## Slide 29: Principles of reliable data transfer
important in application, transport, link layers
  top-10 list of important networking topics!
characteristics of unreliable channel will determine complexity of reliable data transfer protocol (rdt)

## Slide 30: Principles of reliable data transfer
characteristics of unreliable channel will determine complexity of reliable data transfer protocol (rdt)
important in application, transport, link layers
  top-10 list of important networking topics!

## Slide 31: Principles of reliable data transfer
characteristics of unreliable channel will determine complexity of reliable data transfer protocol (rdt)
important in application, transport, link layers
  top-10 list of important networking topics!

## Slide 32: Reliable data transfer: getting started
send
side
receive
side
rdt_send(): called from above (e.g., by app-layer). Passes data to be delivered to receiver’s upper layer
udt_send(): called by rdt,
to transfer packet over
unreliable channel to receiver
rdt_rcv(): called when packet arrives on rcv-side of channel
deliver_data(): called by rdt to deliver data to upper

## Slide 33: Reliable data transfer: getting started
We’ll:
incrementally develop sender, receiver sides of reliable data transfer protocol (rdt)
consider only unidirectional data transfer
  but control info will flow on both directions!
use finite state machines (FSM) to specify sender, receiver
state
1
state
2
event causing state transition
actions taken on state transition
state: when in this “state” next state uniquely determined by next event
event
actions
Notes: RDT1.0
for ideal environment
  No errors
  No losses
Sender always receives all bits and packets
RDT 2.0
  Assumption of no packet loss
  But there are errors we now look for acknowledgement messages.
  ACK= acknowledgment
  NAK = Negative Acknowledgements
  if there are errors send NAK. Otherwise send ACK

## Slide 34: rdt1.0: reliable transfer over a reliable channel
underlying channel perfectly reliable
  no bit errors
  no loss of packets
separate FSMs for sender, receiver:
  sender sends data into underlying channel
  receiver reads data from underlying channel
Wait for call from above
packet = make_pkt(data)
udt_send(packet)
rdt_send(data)
extract (packet,data)
deliver_data(data)
Wait for call from below
rdt_rcv(packet)
sender
receiver

## Slide 35: rdt2.0: channel with bit errors
underlying channel may flip bits in packet
  checksum to detect bit errors
the question: how to recover from errors:
  acknowledgements (ACKs): receiver explicitly tells sender that pkt received OK
  negative acknowledgements (NAKs): receiver explicitly tells sender that pkt had errors
  sender retransmits pkt on receipt of NAK
new mechanisms in rdt2.0 (beyond rdt1.0):
  error detection
  receiver feedback: control msgs (ACK,NAK) rcvr->sender
How do humans recover from “errors”
during conversation?

## Slide 36: rdt2.0: channel with bit errors
underlying channel may flip bits in packet
  checksum to detect bit errors
the question: how to recover from errors:
  acknowledgements (ACKs): receiver explicitly tells sender that pkt received OK
  negative acknowledgements (NAKs): receiver explicitly tells sender that pkt had errors
  sender retransmits pkt on receipt of NAK
new mechanisms in rdt2.0 (beyond rdt1.0):
  error detection
  feedback: control msgs (ACK,NAK) from receiver to sender

## Slide 37: rdt2.0: FSM specification
Wait for call from above
sndpkt = make_pkt(data, checksum)
udt_send(sndpkt)
extract(rcvpkt,data)
deliver_data(data)
udt_send(ACK)
rdt_rcv(rcvpkt) &&
notcorrupt(rcvpkt)
rdt_rcv(rcvpkt) && isACK(rcvpkt)
udt_send(sndpkt)
rdt_rcv(rcvpkt) &&
isNAK(rcvpkt)
udt_send(NAK)
rdt_rcv(rcvpkt) &&
corrupt(rcvpkt)
Wait for ACK or NAK
Wait for call from below
sender
receiver
rdt_send(data)
L

## Slide 38: rdt2.0: operation with no errors
Wait for call from above
sndpkt = make_pkt(data, checksum)
udt_send(sndpkt)
extract(rcvpkt,data)
deliver_data(data)
udt_send(ACK)
rdt_rcv(rcvpkt) &&
notcorrupt(rcvpkt)
rdt_rcv(rcvpkt) && isACK(rcvpkt)
udt_send(sndpkt)
rdt_rcv(rcvpkt) &&
isNAK(rcvpkt)
udt_send(NAK)
rdt_rcv(rcvpkt) &&
corrupt(rcvpkt)
Wait for ACK or NAK
Wait for call from below
rdt_send(data)
L

## Slide 39: rdt2.0: error scenario
Wait for call from above
sndpkt = make_pkt(data, checksum)
udt_send(sndpkt)
extract(rcvpkt,data)
deliver_data(data)
udt_send(ACK)
rdt_rcv(rcvpkt) &&
notcorrupt(rcvpkt)
rdt_rcv(rcvpkt) && isACK(rcvpkt)
udt_send(sndpkt)
rdt_rcv(rcvpkt) &&
isNAK(rcvpkt)
udt_send(NAK)
rdt_rcv(rcvpkt) &&
corrupt(rcvpkt)
Wait for ACK or NAK
Wait for call from below
rdt_send(data)
L

## Slide 40: rdt2.0 has a fatal flaw!
what happens if ACK/NAK corrupted?
sender doesn’t know what happened at receiver!
can’t just retransmit: possible duplicate
handling duplicates:
sender retransmits current pkt if ACK/NAK corrupted
sender adds sequence number to each pkt
receiver discards (doesn’t deliver up) duplicate pkt
stop and wait
sender sends one packet,
then waits for receiver
response

## Slide 41: rdt2.1: sender, handles garbled ACK/NAKs
Wait for call 0 from above
sndpkt = make_pkt(0, data, checksum)
udt_send(sndpkt)
rdt_send(data)
Wait for ACK or NAK 0
udt_send(sndpkt)
rdt_rcv(rcvpkt) &&
( corrupt(rcvpkt) ||
isNAK(rcvpkt) )
sndpkt = make_pkt(1, data, checksum)
udt_send(sndpkt)
rdt_send(data)
rdt_rcv(rcvpkt)
&& notcorrupt(rcvpkt)
&& isACK(rcvpkt)
udt_send(sndpkt)
rdt_rcv(rcvpkt) &&
( corrupt(rcvpkt) ||
isNAK(rcvpkt) )
rdt_rcv(rcvpkt)
&& notcorrupt(rcvpkt)
&& isACK(rcvpkt)
Wait for
call 1 from above
Wait for ACK or NAK 1
L
L

## Slide 42: rdt2.1: receiver, handles garbled ACK/NAKs
Wait for
0 from below
sndpkt = make_pkt(NAK, chksum)
udt_send(sndpkt)
rdt_rcv(rcvpkt) &&
not corrupt(rcvpkt) &&
has_seq0(rcvpkt)
rdt_rcv(rcvpkt) && notcorrupt(rcvpkt)
&& has_seq1(rcvpkt)
extract(rcvpkt,data)
deliver_data(data)
sndpkt = make_pkt(ACK, chksum)
udt_send(sndpkt)
Wait for
1 from below
rdt_rcv(rcvpkt) && notcorrupt(rcvpkt)
&& has_seq0(rcvpkt)
extract(rcvpkt,data)
deliver_data(data)
sndpkt = make_pkt(ACK, chksum)
udt_send(sndpkt)
rdt_rcv(rcvpkt) && (corrupt(rcvpkt)
sndpkt = make_pkt(ACK, chksum)
udt_send(sndpkt)
rdt_rcv(rcvpkt) &&
not corrupt(rcvpkt) &&
has_seq1(rcvpkt)
rdt_rcv(rcvpkt) && (corrupt(rcvpkt)
sndpkt = make_pkt(ACK, chksum)
udt_send(sndpkt)
sndpkt = make_pkt(NAK, chksum)
udt_send(sndpkt)

## Slide 43: (Question) rdt2.1: sender
Wait for call 0 from above
sndpkt = make_pkt(0, data, checksum)
udt_send(sndpkt)
rdt_send(data)
Wait for ACK or NAK 0
udt_send(sndpkt)
rdt_rcv(rcvpkt) &&
( corrupt(rcvpkt) ||
isNAK(rcvpkt) )
sndpkt = make_pkt(1, data, checksum)
udt_send(sndpkt)
rdt_send(data)
rdt_rcv(rcvpkt)
&& notcorrupt(rcvpkt)
&& isACK(rcvpkt)
udt_send(sndpkt)
rdt_rcv(rcvpkt) &&
( corrupt(rcvpkt) ||
isNAK(rcvpkt) )
rdt_rcv(rcvpkt)
&& notcorrupt(rcvpkt)
&& isACK(rcvpkt)
Wait for
call 1 from above
Wait for ACK or NAK 1
L
L
Please describe the event?

## Slide 44: (Question) rdt2.1: receiver
Wait for
0 from below
sndpkt = make_pkt(NAK, chksum)
udt_send(sndpkt)
rdt_rcv(rcvpkt) &&
not corrupt(rcvpkt) &&
has_seq0(rcvpkt)
rdt_rcv(rcvpkt) && notcorrupt(rcvpkt)
&& has_seq1(rcvpkt)
extract(rcvpkt,data)
deliver_data(data)
sndpkt = make_pkt(ACK, chksum)
udt_send(sndpkt)
Wait for
1 from below
rdt_rcv(rcvpkt) && notcorrupt(rcvpkt)
&& has_seq0(rcvpkt)
extract(rcvpkt,data)
deliver_data(data)
sndpkt = make_pkt(ACK, chksum)
udt_send(sndpkt)
rdt_rcv(rcvpkt) && (corrupt(rcvpkt)
sndpkt = make_pkt(ACK, chksum)
udt_send(sndpkt)
rdt_rcv(rcvpkt) &&
not corrupt(rcvpkt) &&
has_seq1(rcvpkt)
rdt_rcv(rcvpkt) && (corrupt(rcvpkt)
sndpkt = make_pkt(ACK, chksum)
udt_send(sndpkt)
sndpkt = make_pkt(NAK, chksum)
udt_send(sndpkt)
Please describe the event?

## Slide 45: (Question) rdt2.1: receiver
Wait for
0 from below
sndpkt = make_pkt(NAK, chksum)
udt_send(sndpkt)
rdt_rcv(rcvpkt) &&
not corrupt(rcvpkt) &&
has_seq0(rcvpkt)
rdt_rcv(rcvpkt) && notcorrupt(rcvpkt)
&& has_seq1(rcvpkt)
extract(rcvpkt,data)
deliver_data(data)
sndpkt = make_pkt(ACK, chksum)
udt_send(sndpkt)
Wait for
1 from below
rdt_rcv(rcvpkt) && notcorrupt(rcvpkt)
&& has_seq0(rcvpkt)
extract(rcvpkt,data)
deliver_data(data)
sndpkt = make_pkt(ACK, chksum)
udt_send(sndpkt)
rdt_rcv(rcvpkt) && (corrupt(rcvpkt)
sndpkt = make_pkt(ACK, chksum)
udt_send(sndpkt)
rdt_rcv(rcvpkt) &&
not corrupt(rcvpkt) &&
has_seq1(rcvpkt)
rdt_rcv(rcvpkt) && (corrupt(rcvpkt)
sndpkt = make_pkt(ACK, chksum)
udt_send(sndpkt)
sndpkt = make_pkt(NAK, chksum)
udt_send(sndpkt)
Please describe the event?

## Slide 46: rdt2.1: discussion
sender:
seq # added to pkt
two seq. #’s (0,1) will suffice. Why?
must check if received ACK/NAK corrupted
twice as many states
  state must “remember” whether “expected” pkt should have seq # of 0 or 1
receiver:
must check if received packet is duplicate
  state indicates whether 0 or 1 is expected pkt seq #
note: receiver can not know if its last ACK/NAK received OK at sender
It allows the receiver to know whether the sender
is resending the previously transmitted packet
(the sequence number of the received packet has
the same sequence number as the most recently
received packet) or a new packet (the sequence
number changes).

## Slide 47: rdt2.1: discussion
sender:
seq # added to pkt
two seq. #’s (0,1) will suffice. Why?
must check if received ACK/NAK corrupted
twice as many states
  state must “remember” whether “expected” pkt should have seq # of 0 or 1
receiver:
must check if received packet is duplicate
  state indicates whether 0 or 1 is expected pkt seq #
note: receiver can not know if its last ACK/NAK received OK at sender
Q. How does the sender check if received ACK/NAK corrupted?

## Slide 48: rdt2.1: discussion
sender:
seq # added to pkt
two seq. #’s (0,1) will suffice. Why?
must check if received ACK/NAK corrupted
twice as many states
  state must “remember” whether “expected” pkt should have seq # of 0 or 1
receiver:
must check if received packet is duplicate
  state indicates whether 0 or 1 is expected pkt seq #
note: receiver can not know if its last ACK/NAK received OK at sender
Q. How does the
receiver check if received packet is duplicate?

## Slide 49: rdt2.1: discussion
sender:
seq # added to pkt
two seq. #’s (0,1) will suffice. Why?
must check if received ACK/NAK corrupted
twice as many states
  state must “remember” whether “expected” pkt should have seq # of 0 or 1
receiver:
must check if received packet is duplicate
  state indicates whether 0 or 1 is expected pkt seq #
note: receiver can not know if its last ACK/NAK received OK at sender
Q. Why does the sender may send duplicated packet? Or in which case?

## Slide 50: rdt2.2: a NAK-free protocol
same functionality as rdt2.1, using ACKs only
instead of NAK, receiver sends ACK for last pkt received OK
  receiver must explicitly include seq # of pkt being ACKed
duplicate ACK at sender results in same action as NAK: retransmit current pkt

## Slide 51: rdt2.2: sender, receiver fragments
Wait for call 0 from above
sndpkt = make_pkt(0, data, checksum)
udt_send(sndpkt)
rdt_send(data)
udt_send(sndpkt)
rdt_rcv(rcvpkt) &&
( corrupt(rcvpkt) ||
isACK(rcvpkt,1) )
rdt_rcv(rcvpkt)
&& notcorrupt(rcvpkt)
&& isACK(rcvpkt,0)
Wait for ACK
0
sender FSM
fragment
rdt_rcv(rcvpkt) && notcorrupt(rcvpkt)
&& has_seq1(rcvpkt)
extract(rcvpkt,data)
deliver_data(data)
sndpkt = make_pkt(ACK1, chksum)
udt_send(sndpkt)
Wait for
0 from below
rdt_rcv(rcvpkt) &&
(corrupt(rcvpkt) ||
has_seq1(rcvpkt))
udt_send(sndpkt)
receiver FSM
fragment
L

## Slide 52: rdts 1.0, 2.0, 2.1, 2.2
rdt 1.0
  No pkt loss, No pkt error (corruption)
rdt 2.0
  No pkt loss
  Pkt error  Use ACK/NAK
  No ACK/NAK corruptions
rdt 2.1
  No pkt loss
  Pkt error, Use ACK/NAK
  ACK/NAK corruptions  Use sequence #s on pkts
rdt 2.2
  same as rdt2.1, using ACKs only
  Use sequence #s on ACKs, too.

## Slide 53: rdt3.0: channels with errors and loss
new assumption: underlying channel can also lose packets (data, ACKs)
  checksum, seq. #, ACKs, retransmissions will be of help … but not enough
approach: sender waits “reasonable” amount of time for ACK
retransmits if no ACK received in this time
if pkt (or ACK) just delayed (not lost):
  retransmission will be duplicate, but seq. #’s already handles this
  receiver must specify seq # of pkt being ACKed
requires countdown timer

## Slide 54: rdt3.0 sender
sndpkt = make_pkt(0, data, checksum)
udt_send(sndpkt)
start_timer
rdt_send(data)
Wait for ACK0
rdt_rcv(rcvpkt) &&
( corrupt(rcvpkt) ||
isACK(rcvpkt,1) )
Wait for
call 1 from above
sndpkt = make_pkt(1, data, checksum)
udt_send(sndpkt)
start_timer
rdt_send(data)
rdt_rcv(rcvpkt)
&& notcorrupt(rcvpkt)
&& isACK(rcvpkt,0)
rdt_rcv(rcvpkt) &&
( corrupt(rcvpkt) ||
isACK(rcvpkt,0) )
rdt_rcv(rcvpkt)
&& notcorrupt(rcvpkt)
&& isACK(rcvpkt,1)
stop_timer
stop_timer
udt_send(sndpkt)
start_timer
timeout
udt_send(sndpkt)
start_timer
timeout
rdt_rcv(rcvpkt)
Wait for
call 0from above
Wait for ACK1
L
rdt_rcv(rcvpkt)
L
L
L

## Slide 55: rdt3.0 in action
sender
receiver
rcv pkt1
rcv pkt0
send ack0
send ack1
send ack0
rcv ack0
send pkt0
send pkt1
rcv ack1
send pkt0
rcv pkt0
pkt0
pkt0
pkt1
ack1
ack0
ack0
(a) no loss
sender
receiver
rcv pkt1
rcv pkt0
send ack0
send ack1
send ack0
rcv ack0
send pkt0
send pkt1
rcv ack1
send pkt0
rcv pkt0
pkt0
pkt0
ack1
ack0
ack0
(b) packet loss
pkt1
X
loss
pkt1
timeout
resend pkt1
Notes: after the timer expires
after a given amount of timer has expired

## Slide 56: rdt3.0 in action
rcv pkt1
send ack1
(detect duplicate)
pkt1
sender
receiver
rcv pkt1
rcv pkt0
send ack0
send ack1
send ack0
rcv ack0
send pkt0
send pkt1
rcv ack1
send pkt0
rcv pkt0
pkt0
pkt0
ack1
ack0
ack0
(c) ACK loss
ack1
X
loss
pkt1
timeout
resend pkt1
rcv pkt1
send ack1
(detect duplicate)
pkt1
sender
receiver
rcv pkt1
send ack0
rcv ack0
send pkt1
send pkt0
rcv pkt0
pkt0
ack0
(d) premature timeout/ delayed ACK
pkt1
timeout
resend pkt1
ack1
send ack1
send pkt0
rcv ack1
pkt0
ack1
ack0
send pkt0
rcv ack1
pkt0
rcv pkt0
send ack0
ack0
rcv pkt0
send ack0
(detect duplicate)

## Slide 57: rdt3.0 in action
rcv pkt1
send ack1
(detect duplicate)
pkt1
sender
receiver
rcv pkt1
rcv pkt0
send ack0
send ack1
send ack0
rcv ack0
send pkt0
send pkt1
rcv ack1
send pkt0
rcv pkt0
pkt0
pkt0
ack1
ack0
ack0
(c) ACK loss
ack1
X
loss
pkt1
timeout
resend pkt1
rcv pkt1
send ack1
(detect duplicate)
pkt1
sender
receiver
rcv pkt1
send ack0
rcv ack0
send pkt1
send pkt0
rcv pkt0
pkt0
ack0
(d) premature timeout/ delayed ACK
pkt1
timeout
resend pkt1
ack1
send ack1
send pkt0
rcv ack1
pkt0
ack1
ack0
send pkt0
rcv ack1
pkt0
rcv pkt0
send ack0
ack0
rcv pkt0
send ack0
(detect duplicate)
A
A
B
B
B
B
C
C
C
C
Waits for ACK-0
Waits for ACK-1
C
B
A

## Slide 58: rdt (reliable data transfer) protocols:
sender sends one packet,
then waits for receiver response
stop and wait protocols!

## Slide 59: Pipelined protocols
pipelining: sender allows multiple, “in-flight”, yet-to-be-acknowledged pkts
  range of sequence numbers must be increased
  buffering at sender and/or receiver
two generic forms of pipelined protocols: go-Back-N, selective repeat
Notes: two generic forms of pipelined protocols:
go-Back-N
selective repeat

## Slide 60: Pipelining: increased utilization
first packet bit transmitted, t = 0
sender
receiver
RTT
last bit transmitted, t = L / R
first packet bit arrives
last packet bit arrives, send ACK
ACK arrives, send next
packet, t = RTT + L / R
last bit of 2nd packet arrives, send ACK
last bit of 3rd packet arrives, send ACK
3-packet pipelining increases
utilization by a factor of 3!

## Slide 61: Pipelined protocols: overview
Go-back-N:
sender can have up to N unacked packets in pipeline
receiver only sends cumulative ack
  doesn’t ack packet if there’s a gap
sender has timer for oldest unacked packet
  when timer expires, retransmit ‘all’ unacked packets
Selective Repeat:
sender can have up to N unacked packets in pipeline
receiver sends individual ack for each packet
sender maintains timer for each unacked packet
  when timer expires, retransmit only ‘that’ unacked packet

## Slide 62: Go-Back-N: sender
k-bit seq # in pkt header
“window” of up to N, consecutive unack’ed pkts allowed
ACK(n): ACKs all pkts up to, including seq # n – “cumulative ACK”
  may receive duplicate ACKs (see receiver)
timer for oldest in-flight pkt
timeout(n): retransmit packet n and all higher seq # pkts in window

## Slide 63: GBN: sender extended FSM
Wait
start_timer
udt_send(sndpkt[base])
udt_send(sndpkt[base+1])
…
udt_send(sndpkt[nextseqnum-1])
timeout
rdt_send(data)
if (nextseqnum < base+N) {
sndpkt[nextseqnum] = make_pkt(nextseqnum,data,chksum)
udt_send(sndpkt[nextseqnum])
if (base == nextseqnum)
start_timer
nextseqnum++
}
else
refuse_data(data)
base = getacknum(rcvpkt)+1
If (base == nextseqnum)
stop_timer
else
start_timer
rdt_rcv(rcvpkt) &&
notcorrupt(rcvpkt)
base=1
nextseqnum=1
rdt_rcv(rcvpkt)
&& corrupt(rcvpkt)
L

## Slide 64: GBN: receiver extended FSM
Wait
udt_send(sndpkt)
default
rdt_rcv(rcvpkt)
&& notcurrupt(rcvpkt)
&& hasseqnum(rcvpkt,expectedseqnum)
extract(rcvpkt,data)
deliver_data(data)
sndpkt = make_pkt(expectedseqnum,ACK,chksum)
udt_send(sndpkt)
expectedseqnum++
expectedseqnum=1
sndpkt =
make_pkt(expectedseqnum,ACK,chksum)
L
ACK-only: always send ACK for correctly-received pkt with highest in-order seq #
  may generate duplicate ACKs
  need only remember expectedseqnum
out-of-order pkt:
  discard (don’t buffer): no receiver buffering!
  re-ACK pkt with highest in-order seq #

## Slide 65: GBN in action
send pkt0
send pkt1
send pkt2
send pkt3
(wait)
sender
receiver
receive pkt0, send ack0
receive pkt1, send ack1
receive pkt3, discard,
(re)send ack1
rcv ack0, send pkt4
rcv ack1, send pkt5
pkt 2 timeout
send pkt2
send pkt3
send pkt4
send pkt5
X
loss
receive pkt4, discard,
(re)send ack1
receive pkt5, discard,
(re)send ack1
rcv pkt2, deliver, send ack2
rcv pkt3, deliver, send ack3
rcv pkt4, deliver, send ack4
rcv pkt5, deliver, send ack5
ignore duplicate ACK
0 1 2 3 4 5 6 7 8
sender window (N=4)
0 1 2 3 4 5 6 7 8
0 1 2 3 4 5 6 7 8
0 1 2 3 4 5 6 7 8
0 1 2 3 4 5 6 7 8
0 1 2 3 4 5 6 7 8
0 1 2 3 4 5 6 7 8
0 1 2 3 4 5 6 7 8
0 1 2 3 4 5 6 7 8
0 1 2 3 4 5 6 7 8

## Slide 66: GBN in action
send pkt0
send pkt1
send pkt2
send pkt3
(wait)
sender
receiver
receive pkt0, send ack0
receive pkt1, send ack1
receive pkt3, discard,
(re)send ack1
rcv ack0, send pkt4
rcv ack1, send pkt5
pkt 2 timeout
send pkt2
send pkt3
send pkt4
send pkt5
loss
X
receive pkt4, discard,
(re)send ack1
receive pkt5, discard,
(re)send ack1
rcv pkt2, deliver, send ack2
rcv pkt3, deliver, send ack3
rcv pkt4, deliver, send ack4
rcv pkt5, deliver, send ack5
ignore duplicate ACK
0 1 2 3 4 5 6 7 8
sender window (N=4)
0 1 2 3 4 5 6 7 8
0 1 2 3 4 5 6 7 8
0 1 2 3 4 5 6 7 8
0 1 2 3 4 5 6 7 8
0 1 2 3 4 5 6 7 8
0 1 2 3 4 5 6 7 8
0 1 2 3 4 5 6 7 8
0 1 2 3 4 5 6 7 8
0 1 2 3 4 5 6 7 8
Wait for one or more of these packets to be acknowledged before proceeding.
Notes: The number of sequence numbers must be greater than the window: side N
“ the #. Seq #s >= N”
EXAM QUESTION: WHAT ACK NUMBERS IS THERECEIVER SENDING.

## Slide 67: GBN: Example
Click: GBN Animation (YouTube)

## Slide 68: Selective repeat
receiver individually acknowledges all correctly received pkts
  buffers pkts, as needed, for eventual in-order delivery to upper layer
sender only resends pkts for which ACK not received
  sender timer for each unACKed pkt
sender window
  N consecutive seq #’s
  limits seq #s of sent, unACKed pkts

## Slide 69: Selective repeat: sender, receiver windows

## Slide 70: Selective repeat
data from above:
if next available seq # in window, send pkt
timeout(n):
resend pkt n, restart timer
ACK(n) in [sendbase,sendbase+N]:
mark pkt n as received
if n smallest unACKed pkt, advance window base to next unACKed seq #
sender
pkt n in [rcvbase, rcvbase+N-1]
send ACK(n)
out-of-order: buffer
in-order: deliver (also deliver buffered, in-order pkts), advance window to next not-yet-received pkt
pkt n in [rcvbase-N,rcvbase-1]
ACK(n)
otherwise:
ignore
receiver

## Slide 71: Selective repeat in action
send pkt0
send pkt1
send pkt2
send pkt3
(wait)
sender
receiver
receive pkt0, send ack0
receive pkt1, send ack1
receive pkt3, buffer,
send ack3
rcv ack0, send pkt4
rcv ack1, send pkt5
pkt 2 timeout
send pkt2
X
loss
receive pkt4, buffer,
send ack4
receive pkt5, buffer,
send ack5
rcv pkt2; deliver pkt2,
pkt3, pkt4, pkt5; send ack2
record ack3 arrived
0 1 2 3 4 5 6 7 8
sender window (N=4)
0 1 2 3 4 5 6 7 8
0 1 2 3 4 5 6 7 8
0 1 2 3 4 5 6 7 8
0 1 2 3 4 5 6 7 8
0 1 2 3 4 5 6 7 8
0 1 2 3 4 5 6 7 8
0 1 2 3 4 5 6 7 8
0 1 2 3 4 5 6 7 8
0 1 2 3 4 5 6 7 8
record ack4 arrived
record ack5 arrived
Q: what happens when ack2 arrives?
Notes: The windows size must be less than or equal to half the sequence number space for SR protocols.

## Slide 72: Selective repeat: dilemma
example:
seq #’s: 0, 1, 2, 3
window size=3
receiver window
(after receipt)
sender window
(after receipt)
0 1 2 3 0 1 2
0 1 2 3 0 1 2
0 1 2 3 0 1 2
pkt0
pkt1
pkt2
0 1 2 3 0 1 2
pkt0
timeout
retransmit pkt0
0 1 2 3 0 1 2
0 1 2 3 0 1 2
0 1 2 3 0 1 2
X
X
X
will accept packet
with seq number 0
(b) oops!
0 1 2 3 0 1 2
0 1 2 3 0 1 2
0 1 2 3 0 1 2
pkt0
pkt1
pkt2
0 1 2 3 0 1 2
pkt0
0 1 2 3 0 1 2
0 1 2 3 0 1 2
0 1 2 3 0 1 2
X
will accept packet
with seq number 0
0 1 2 3 0 1 2
pkt3
(a) no problem
receiver can’t see sender side.
receiver behavior identical in both cases!
Something’s (very) wrong!
receiver sees no difference in two scenarios!
duplicate data accepted as new in (b)
Q: what relationship between seq # size and window size to avoid problem in (b)?