## Slide 1
Chapter 2 Application Layer
Computer Networking: A Top Down Approach 6th edition Jim Kurose, Keith Ross Addison-Wesley March 2012
A note on the use of these ppt slides:
We’re making these slides freely available to all (faculty, students, readers). They’re in PowerPoint form so you see the animations; and can add, modify, and delete slides (including this one) and slide content to suit your needs. They obviously represent a lot of work on our part. In return for use, we only ask the following:
If you use these slides (e.g., in a class) that you mention their source (after all, we’d like people to use our book!)
If you post any slides on a www site, that you note that they are adapted from (or perhaps identical to) our slides, and note our copyright of this material.
Thanks and enjoy! JFK/KWR
All material copyright 1996-2012
J.F Kurose and K.W. Ross, All Rights Reserved

## Slide 2: Chapter 2
Course Objectives:
  Gaining factual knowledge (terminology, classifications, methods, trends) on computer networks
    Gain factual knowledge, including Web, Http, Ftp, SMTP, DNS, P2P and Socket programming.
  Learning fundamental principles, generalizations, or theories in computer networks
    Get to know the principles of networking applications.

## Slide 3: Chapter 2: outline
2.1 Principles of Network applications
2.2 Web and HTTP
2.3 FTP
2.4 electronic mail
  SMTP, POP3, IMAP
2.5 DNS
2.6 P2P applications
2.7 socket programming with UDP and TCP

## Slide 4: Chapter 2: application layer
2.1 Principles of Network Applications
Network application architectures
Processes communicating
Application-layer protocols
Transport services available to applications
Transport services provided by the Internet

## Slide 5: Chapter 2: application layer
our goals:
conceptual, implementation aspects of network application protocols
  transport-layer service models
  client-server paradigm
  peer-to-peer paradigm
learn about protocols by examining popular application-level protocols
  HTTP
  FTP
  SMTP / POP3 / IMAP
  DNS
creating network applications
  socket API

## Slide 6: Some network apps
e-mail
web
text messaging
remote login
P2P file sharing
multi-user network games
streaming stored video (YouTube, Hulu, Netflix)
voice over IP (e.g., Skype)
real-time video conferencing
social networking
search
…
…

## Slide 7: Creating a network app
write programs that:
run on (different) end systems
communicate over network
e.g., web server software communicates with browser software
no need to write software for network-core devices
network-core devices do not run user applications
applications on end systems allows for rapid app development, propagation
application
transport
network
data link
physical
application
transport
network
data link
physical
application
transport
network
data link
physical

## Slide 8: Application architectures
possible structure of applications:
(1) client-server
(2) peer-to-peer (P2P)

## Slide 9: (1) Client-server architecture
server:
always-on host
permanent IP address
data centers for scaling
clients:
communicate with server
may be intermittently connected
may have dynamic IP addresses
do not communicate directly with each other (e.g. two browsers)
client/server

## Slide 10: Application architectures
possible structure of applications:
(1) client-server
(2) peer-to-peer (P2P)

## Slide 11: (2) P2P architecture
no always-on server
arbitrary end systems directly communicate
peers request service from other peers, provide service in return to other peers
  self scalability – new peers bring new service capacity, as well as new service demands
peers are intermittently connected and change IP addresses
  complex management
peer-peer

## Slide 12: Chapter 2: application layer
2.1 Principles of Network Applications
Network application architectures
Processes communicating
Application-layer protocols
Transport services available to applications
Transport services provided by the Internet

## Slide 13: Processes communicating
process: program running within a host
within same host, two processes communicate using inter-process communication (defined by OS)
processes in different hosts communicate by exchanging messages
client process: process that initiates communication
server process: process that waits to be contacted
aside: applications with P2P architectures have client processes & server processes
clients, servers

## Slide 14: Sockets
process sends/receives messages to/from its socket
socket analogous to door
  sending process shoves message out door
  sending process relies on transport infrastructure on other side of door to deliver message to socket at receiving process
Internet
controlled
by OS
controlled by
app developer
transport
application
physical
link
network
process
transport
application
physical
link
network
process
socket
Notes: Socket connects your process to the transport layer. (not a port. )

## Slide 15: Addressing processes
Receiving process must have an address (identifier).
  host device has unique 32-bit IP address (Chapter 4)
  Q: does IP address of host on which process runs suffice for identifying the process?
identifier includes both IP address and port numbers associated with process on host.
example port numbers:
  HTTP server: 80
  mail server: 25
to send HTTP message to gaia.cs.umass.edu web server:
  IP address: 128.119.245.12
  port number: 80
more shortly…
Port numbers will be covered in Chapter 3.
    A: no, many processes can be running on same host
Notes: Https: 443

## Slide 16: Chapter 2: application layer
2.1 Principles of Network Applications
Network application architectures
Processes communicating
Application-layer protocols
Transport services available to applications
Transport services provided by the Internet

## Slide 17: App-layer protocols
We have just learned:
  Network processes communicate with each other by sending messages into sockets.
How are these messages structured?
What are the meanings of the various fields in the messages?
When do the processes send the messages?
Application-layer protocols define this!

## Slide 18: App-layer protocol defines
types of messages exchanged,
  e.g., request, response
message syntax:
  what fields in messages & how fields are delineated
message semantics
  meaning of information in fields
rules for when and how processes send & respond to messages
open protocols:
defined in RFCs (Request For Comments)
allows for interoperability
e.g., HTTP, SMTP
proprietary protocols:
e.g., Skype

## Slide 19: Network application vs. App-layer protocols
Distinguish between network applications and application-layer protocols!  App-layer protocol is only one piece of network application!
Examples
  Web application consists of:
    HTTP, Web browsers (chrome, etc), Web servers, etc
  Internet email application consists of:
    SMTP, Mail clients (outlook, etc), Mail servers, etc

## Slide 20: Chapter 2: application layer
2.1 Principles of Network Applications
Network application architectures
Processes communicating
Application-layer protocols
Transport services available to applications
Transport services provided by the Internet

## Slide 21: Transport services available to applications
Recall:
  A socket is the interface between the application process and the transport-layer protocol.
  Sender (application) pushes messages through the socket.
  At the other side of the socket, the transport-layer protocol has the responsibility of getting the messages to the socket of the receiver (application).
Internet
controlled
by OS
controlled by
app developer
transport
application
physical
link
network
process
transport
application
physical
link
network
process
socket

## Slide 22: Transport services available to applications
When developing an application:
  What transport-layer protocol will you use?
    Pick the protocol with the services that best match your application’s need.
    E.g. What transport service will your message use? “train” or “airplane”?
Internet
controlled
by OS
controlled by
app developer
transport
application
physical
link
network
process
transport
application
physical
link
network
process
socket

## Slide 23: What are the services that a transport-layer protocol can offer to applications?
data integrity
some apps (e.g., file transfer, web transactions) require 100% reliable data transfer
other apps (e.g., audio) can tolerate some loss
timing
some apps (e.g., Internet telephony, interactive games) require low delay to be “effective”
throughput
some apps (e.g., multimedia) require minimum amount of throughput to be “effective”
other apps (“elastic apps”) make use of whatever throughput they get
security
encryption, data integrity, …

## Slide 24: Transport service requirements: common apps
application
file transfer
e-mail
Web documents
real-time audio/video
stored audio/video
interactive games
text messaging
data loss
no loss
no loss
no loss
loss-tolerant
loss-tolerant
loss-tolerant
no loss
throughput
elastic
elastic
elastic
audio: 5kbps-1Mbps
video:10kbps-5Mbps
same as above
few kbps up
elastic
time sensitive
no
no
no
yes, 100’s msec
yes, few secs
yes, 100’s msec
yes and no

## Slide 25: Chapter 2: application layer
2.1 Principles of Network Applications
Network application architectures
Processes communicating
Application-layer protocols
Transport services available to applications
Transport services provided by the Internet

## Slide 26: Internet transport protocols services
TCP service:
reliable transport between sending and receiving process
flow control: sender won’t overwhelm receiver
congestion control: throttle sender when network overloaded
does not provide: timing, minimum throughput guarantee, security
connection-oriented: setup required between client and server processes
UDP service:
unreliable data transfer between sending and receiving process
does not provide: reliability, flow control, congestion control, timing, throughput guarantee, security, connection setup,
Q: why bother? Why is there a UDP?
Notes: A:

## Slide 27: Internet apps: application, transport protocols
application
e-mail
remote terminal access
Web
file transfer
streaming multimedia
Internet telephony
application
layer protocol
SMTP [RFC 2821]
Telnet [RFC 854]
HTTP [RFC 2616]
FTP [RFC 959]
HTTP (e.g., YouTube), RTP [RFC 1889]
SIP, RTP, proprietary
(e.g., Skype)
underlying
transport protocol
TCP
TCP
TCP
TCP
TCP or UDP
TCP or UDP

## Slide 28: Chapter 2: outline
2.1 Principles of Network applications
2.2 Web and HTTP
2.3 FTP
2.4 electronic mail
  SMTP, POP3, IMAP
2.5 DNS
2.6 P2P applications
2.7 socket programming with UDP and TCP

## Slide 29: Web and HTTP
First, let’s review some Web terminology…
web page consists of objects
object can be HTML file, JPEG image, Java applet, audio file,…
Most web pages consist of base HTML-file which includes several referenced objects
each object is addressable by a URL, e.g.,
www.someschool.edu/someDept/pic.gif
host name
path name

## Slide 30: HTTP overview
HTTP: hypertext transfer protocol
Web’s application layer protocol
client/server model
  client: browser that requests, receives, (using HTTP protocol) and “displays” Web objects
  server: Web server sends (using HTTP protocol) objects in response to requests
Defines
  how Web clients request Web objects from Web servers
  how Web servers transfer Web pages to clients
PC running
Firefox browser
server
running
Apache Web
server
iphone running
Safari browser
HTTP request
HTTP response
HTTP request
HTTP response

## Slide 31: HTTP overview (continued)
uses TCP:
Client initiates TCP connection (creates socket) to server.
Server accepts TCP connection from client.
HTTP messages (application-layer protocol messages) exchanged between browser (HTTP client) and Web server (HTTP server).
TCP connection closed.
HTTP is “stateless”
server maintains no information about past client requests
protocols that maintain “state” are complex!
past history (state) must be maintained
if server/client crashes, their views of “state” may be inconsistent, must be reconciled
aside

## Slide 32: HTTP connections
Application developers have to decide which transport service their application will use.
  TCP or UDP?
With TCP:
  Application developers have to make important decisions, again!
    Should each request/response pair be sent over a separate TCP connection?
    Should all of the requests/responses be sent over the same TCP connection?

## Slide 33: HTTP connections
non-persistent HTTP
at most one object sent over TCP connection
  connection then closed
downloading multiple objects required multiple connections
persistent HTTP
multiple objects can be sent over single TCP connection between client, server

## Slide 34: Non-persistent HTTP
suppose user enters URL:
1a. HTTP client initiates TCP connection to HTTP server (process) at www.someSchool.edu on port 80
2. HTTP client sends HTTP request message (containing URL) into TCP connection socket. Message indicates that client wants object someDepartment/home.index
1b. HTTP server at host www.someSchool.edu waiting for TCP connection at port 80. “accepts” connection, notifying client
3. HTTP server receives request message, forms response message containing requested object, and sends message into its socket
time
(contains text,
references to 10
jpeg images)
www.someSchool.edu/someDepartment/home.index

## Slide 35: Non-persistent HTTP (cont.)
5. HTTP client receives response message containing html file, displays html. Parsing html file, finds 10 referenced jpeg objects
6. Steps 1-5 repeated for each of 10 jpeg objects
4. HTTP server closes TCP connection.
time

## Slide 36: Non-persistent HTTP: response time
RTT (definition): time for a small packet to travel from client to server and back
HTTP response time:
one RTT to initiate TCP connection
one RTT for HTTP request and first few bytes of HTTP response to return
file transmission time
non-persistent HTTP response time =
  2RTT+ file transmission time
time to
transmit
file
initiate TCP
connection
RTT
request
file
RTT
file
received
time
time
Round Trip Time

## Slide 37: Persistent HTTP
non-persistent HTTP issues:
requires 2 RTTs per object
OS overhead for each TCP connection
browsers often open parallel TCP connections to fetch referenced objects
persistent HTTP without pipelining:
server leaves connection open after sending response
client issues new request only when previous response has been received
one RTT for each referenced object
persistent HTTP with pipelining:
default in HTTP/1.1
client sends requests as soon as it encounters a referenced object
as little as one RTT for all the referenced objects
Notes: In persistent HTTP without pipelining, the browser first waits to receive a HTTP response from the server before issuing a new HTTP request.
In persistent HTTP with pipelining, the browser issues requests as soon as it has a need to do so, without waiting for response messages from the server. (how most modern browsers run)

## Slide 38: Review Question
Use non-persistent HTTP (single TCP-connection) to access a webpage. In addition to the basic HTML file, the html file refers to 10 JPEG images, two audio clips, and two video clips at the same web server. The round trip time between web browser and the web server is RTT. What is the total response time for the web browser to have all objects? (Ignore file transmission time.)
Use persistent HTTP without pipelining.
Notes: 30 RTT total on non persistant
16 for persistant w/o pipelining

## Slide 39: HTTP request message
two types of HTTP messages: request, response
HTTP request message:
  ASCII (human-readable format)
request line
(GET, POST,
HEAD commands)
header
lines
carriage return,
line feed at start
of line indicates
end of header lines
GET /index.html HTTP/1.1\r\n
Host: www-net.cs.umass.edu\r\n
User-Agent: Firefox/3.6.10\r\n
Accept: text/html,application/xhtml+xml\r\n
Accept-Language: en-us,en;q=0.5\r\n
Accept-Encoding: gzip,deflate\r\n
Accept-Charset: ISO-8859-1,utf-8;q=0.7\r\n
Keep-Alive: 115\r\n
Connection: keep-alive\r\n
\r\n
carriage return character
line-feed character
keep-alive  persistent connection
close  non-persistent connection

## Slide 40: HTTP request message: general format
request
line
header
lines
body
method
sp
sp
cr
lf
version
URL
cr
lf
value
header field name
cr
lf
value
header field name
~
~
~
~
cr
lf
entity body
~
~
~
~

## Slide 41: HTTP response message
status line
(protocol
status code
status phrase)
header
lines
data, e.g.,
requested
HTML file
HTTP/1.1 200 OK\r\n
Date: Sun, 26 Sep 2010 20:09:20 GMT\r\n
Server: Apache/2.0.52 (CentOS)\r\n
Last-Modified: Tue, 30 Oct 2007 17:00:02 GMT\r\n
ETag: "17dc6-a5c-bf716880"\r\n
Accept-Ranges: bytes\r\n
Content-Length: 2652\r\n
Keep-Alive: timeout=10, max=100\r\n
Connection: Keep-Alive\r\n
Content-Type: text/html; charset=ISO-8859-1\r\n
\r\n
data data data data data ...
keep-alive  Will keep the connection
close  Will close the connection

## Slide 42: HTTP response status codes
200 OK
  request succeeded, requested object later in this msg
301 Moved Permanently
  requested object moved, new location specified later in this msg (Location:)
400 Bad Request
  request msg not understood by server
404 Not Found
  requested document not found on this server
505 HTTP Version Not Supported
status code appears in 1st line in server-to-client response message.
some sample codes:

## Slide 43: Trying out HTTP (client side) for yourself
1. Telnet to your favorite Web server:
opens TCP connection to port 80
(default HTTP server port) at cis.poly.edu.
anything typed in sent
to port 80 at cis.poly.edu
telnet cis.poly.edu 80
2. type in a GET HTTP request:
GET /~ross/ HTTP/1.1
Host: cis.poly.edu
by typing this in (hit carriage
return twice), you send
this minimal (but complete)
GET request to HTTP server
3. look at response message sent by HTTP server!
(or use Wireshark to look at captured HTTP request/response)

## Slide 44: User-server state: cookies
many Web sites use cookies
four components:
  1) cookie header line of HTTP response message
  2) cookie header line in next HTTP request message
  3) cookie file kept on user’s host, managed by user’s browser
  4) back-end database at Web site
example:
Susan always access Internet from PC
visits specific e-commerce site for first time
when initial HTTP requests arrives at site, site creates:
  unique ID
  entry in backend database for ID

## Slide 45: Cookies: keeping “state” (cont.)
client
server
usual http response msg
usual http response msg
cookie file
one week later:
usual http request msg
cookie: 1678
cookie-
specific
action
access
ebay 8734
usual http request msg
Amazon server
creates ID
1678 for user
create
entry
usual http response
set-cookie: 1678
ebay 8734
amazon 1678
usual http request msg
cookie: 1678
cookie-
specific
action
access
ebay 8734
amazon 1678
backend
database

## Slide 46: Cookies (continued)
what cookies can be used for:
authorization
shopping carts
recommendations
user session state (Web e-mail)
cookies and privacy:
cookies permit sites to learn a lot about you
you may supply name and e-mail to sites
aside
how to keep “state”:
protocol endpoints: maintain state at sender/receiver over multiple transactions
cookies: http messages carry state

## Slide 47: Web caches (proxy server)
user sets browser: Web accesses via cache
browser sends all HTTP requests to cache
  object in cache: cache returns object
  else cache requests object from origin server, then returns object to client
goal: satisfy client request without involving origin server
client
proxy
server
client
HTTP request
HTTP response
HTTP request
HTTP request
origin
server
origin
server
HTTP response
HTTP response

## Slide 48: More about Web caching
cache acts as both client and server
  server for original requesting client
  client to origin server
typically cache is installed by ISP (university, company, residential ISP)
why Web caching?
reduce response time for client request
reduce traffic on an institution’s access link
Internet dense with caches: enables “poor” content providers to effectively deliver content (so too does P2P file sharing)

## Slide 49: Conditional GET
Goal: don’t send object if cache has up-to-date cached version
  no object transmission delay
  lower link utilization
cache: specify date of cached copy in HTTP request
  If-modified-since: <date>
server: response contains no object if cached copy is up-to-date:
  HTTP/1.0 304 Not Modified
HTTP request msg
If-modified-since: <date>
HTTP response
HTTP/1.0
304 Not Modified
object
not
modified
before
<date>
HTTP request msg
If-modified-since: <date>
HTTP response
HTTP/1.0 200 OK
<data>
object
modified
after
<date>
client
server

## Slide 50: Chapter 2: outline
2.1 principles of network applications
  app architectures
  app requirements
2.2 Web and HTTP
2.3 FTP
2.4 electronic mail
  SMTP, POP3, IMAP
2.5 DNS
2.6 P2P applications
2.7 socket programming with UDP and TCP

## Slide 51: FTP: the file transfer protocol
file transfer
FTP
server
FTP
user
interface
FTP
client
local file
system
remote file
system
user
at host
transfer file to/from remote host
client/server model
  client: side that initiates transfer (either to/from remote)
  server: remote host
ftp: RFC 959
ftp server: port 21
Notes: FTP uses TCP.
Tcp Is a connectiion oriented protocol
Quiz question: Why do we need port numbers? To distinguish processes.

## Slide 52: FTP: separate control, data connections
FTP client contacts FTP server at port 21, using TCP
client authorized over control connection
client browses remote directory, sends commands over control connection
when server receives file transfer command, server opens 2nd TCP data connection (for file) to client
after transferring one file, server closes data connection
FTP
client
FTP
server
TCP control connection,
server port 21
TCP data connection,
server port 20
server opens another TCP data connection to transfer another file
control connection: “out of band”
FTP server maintains “state”: current directory, earlier authentication
Notes: FTP is said to send its control information out-of-band.
In general language, out-of-band refers to communications which occur outside of a previously established communication method or channel.

## Slide 53: FTP commands, responses
sample commands:
sent as ASCII text over control channel
USER username
PASS password
LIST return list of file in current directory
RETR filename retrieves (gets) file
STOR filename stores (puts) file onto remote host
sample return codes
status code and phrase (as in HTTP)
331 Username OK, password required
125 data connection already open; transfer starting
425 Can’t open data connection
452 Error writing file

## Slide 54: Chapter 2: outline
2.1 principles of network applications
  app architectures
  app requirements
2.2 Web and HTTP
2.3 FTP
2.4 electronic mail
  SMTP, POP3, IMAP
2.5 DNS
2.6 P2P applications
2.7 socket programming with UDP and TCP

## Slide 55: Electronic mail
Three major components:
user agents
mail servers
simple mail transfer protocol: SMTP
user agent
a.k.a. “mail reader”
composing, editing, reading mail messages
e.g., Outlook, Thunderbird, iPhone mail client
outgoing, incoming messages stored on server
user mailbox
outgoing
message queue
mail
server
mail
server
mail
server
SMTP
SMTP
SMTP
user
agent
user
agent
user
agent
user
agent
user
agent
user
agent

## Slide 56: Electronic mail: mail servers
mail servers:
mailbox contains incoming messages for user
message queue of outgoing (to be sent) mail messages
SMTP protocol between mail servers to send email messages
  client: sending mail server
  “server”: receiving mail server
mail
server
mail
server
mail
server
SMTP
SMTP
SMTP
user
agent
user
agent
user
agent
user
agent
user
agent
user
agent
user mailbox
outgoing
message queue

## Slide 57: Electronic Mail: SMTP [RFC 2821]
uses TCP to reliably transfer email message from client to server, port 25
direct transfer: sending server to receiving server
three phases of transfer
  handshaking (greeting)
  transfer of messages
  closure
command/response interaction (like HTTP, FTP)
  commands: ASCII text
  response: status code and phrase
messages must be in 7-bit ASCII

## Slide 58: Scenario: Alice sends message to Bob
user
agent
1) Alice uses UA to compose message “to” bob@someschool.edu
2) Alice’s UA sends message to her mail server; message placed in message queue
3) client side of SMTP opens TCP connection with Bob’s mail server
4) SMTP client sends Alice’s message over the TCP connection
5) Bob’s mail server places the message in Bob’s mailbox
6) Bob invokes his user agent to read message
mail
server
mail
server
1
2
3
4
5
6
Alice’s mail server
Bob’s mail server
user
agent

## Slide 59: Sample SMTP interaction
S: 220 hamburger.edu
C: HELO crepes.fr
S: 250 Hello crepes.fr, pleased to meet you
C: MAIL FROM: <alice@crepes.fr>
S: 250 alice@crepes.fr... Sender ok
C: RCPT TO: <bob@hamburger.edu>
S: 250 bob@hamburger.edu ... Recipient ok
C: DATA
S: 354 Enter mail, end with "." on a line by itself
C: Do you like ketchup?
C: How about pickles?
C: .
S: 250 Message accepted for delivery
C: QUIT
S: 221 hamburger.edu closing connection
S:SMTP Server, C:SMTP Client
As soon as the TCP connection is established…
commands
(end of the message)

## Slide 60: SMTP: final words
SMTP uses persistent connections
SMTP requires message (header & body) to be in 7-bit ASCII
SMTP server uses CRLF.CRLF to determine end of message
comparison with HTTP:
HTTP: pull protocol
SMTP: push protocol
both have ASCII command/response interaction, status codes

## Slide 61: SMTP: final words
SMTP uses persistent connections
SMTP requires message (header & body) to be in 7-bit ASCII
SMTP server uses CRLF.CRLF to determine end of message
comparison with HTTP:
HTTP: pull protocol
SMTP: push protocol
both have ASCII command/response interaction, status codes
Someone loads information on a Web server and users use HTTP to pull the information from the server.
TCP connection is initiated by the machine that wants to receive the file.

## Slide 62: SMTP: final words
SMTP uses persistent connections
SMTP requires message (header & body) to be in 7-bit ASCII
SMTP server uses CRLF.CRLF to determine end of message
comparison with HTTP:
HTTP: pull protocol
SMTP: push protocol
both have ASCII command/response interaction, status codes
The sending mail server pushes the file to the receiving mail server.
TCP connection is initiated by the machine that wants to send the file.

## Slide 63: SMTP: final words
SMTP uses persistent connections
SMTP requires message (header & body) to be in 7-bit ASCII
SMTP server uses CRLF.CRLF to determine end of message
comparison with HTTP:
HTTP: pull protocol
SMTP: push protocol
both have ASCII command/response interaction, status codes

## Slide 64: Mail message format
SMTP: protocol for exchanging email msgs
RFC 822: standard for text message format:
header lines, e.g.,
  To:
  From:
  Subject:
  different from SMTP MAIL FROM, RCPT TO: commands!
Body: the “message”
  ASCII characters only
header
body
blank
line

## Slide 65: Mail access protocols
SMTP: delivery/storage to receiver’s server
mail access protocol: retrieval from server
  POP3: Post Office Protocol [RFC 1939]: authorization, download (Port number: 110)
  IMAP: Internet Mail Access Protocol [RFC 1730]: more features, including manipulation of stored msgs on server (Port number: 143)
  HTTP: gmail, Hotmail, Yahoo! Mail, etc.
sender’s mail
server
SMTP
SMTP
mail access
protocol
receiver’s mail
server
(e.g., POP3,
IMAP)
user
agent
user
agent

## Slide 66: POP3 protocol
authorization phase
client commands:
  user: declare username
  pass: password
server responses
  +OK
  -ERR
transaction phase, client:
list: list message numbers
retr: retrieve message by number
dele: delete
quit
C: list
S: 1 498
S: 2 912
S: .
C: retr 1
S: <message 1 contents>
S: .
C: dele 1
C: retr 2
S: <message 2 contents>
S: .
C: dele 2
C: quit
S: +OK POP3 server signing off
S: +OK POP3 server ready
C: user bob
S: +OK
C: pass hungry
S: +OK user successfully logged on

## Slide 67: POP3 (more)
more about POP3
Previous example uses POP3’s “download and delete” mode:
  After a user retrieves its messages from a POP server (the messages are downloaded on the user’s computer), the messages are deleted from the server.
  Bob cannot re-read e-mail if he changes client.
POP3’s “download-and-keep”:
  Messages are not deleted after the user retrieves the messages.
  Copies of messages on different clients.
  When the user retrieves the stored messages from a new machine, all of non-deleted messages will be downloaded to the new machine.
POP3 is stateless across sessions

## Slide 68: IMAP
IMAP
keeps all messages in one place: at server
allows user to organize messages in folders
keeps user state across sessions:
  names of folders and mappings between message IDs and folder name